## Slide 1: ROAD STABILIZATION COMMITTEE
2023-2032 ROAD PROGRAM November 14, 2022

## Slide 2
MUNICIPAL ROAD PROGRAM
ROAD STABILIZATION COMMITTEE
  The largest and perhaps most important asset of municipal infrastructure are the roads. Simply put paved roads are used as a primary mode of transportation and preserving the condition should be a top priority. Municipalities are best served implementing a Pavement Management Plan that uses geographic information system technology to measure and evaluate the road conditions creating comprehensive data. This process allows a municipality to maximize its reinvestment in a feasible manner while maintaining a sound road network.

## Slide 3
PROGRAM PRINCIPAL GUIDELINES
ROAD STABILIZATION COMMITTEE
Spend ~$1.2M annually on Maintenance
Spend Balance on Reconstruction
    ~$500K annually in Neighborhoods (Local)
    Remainder on Main Roads (Operational)
~$60-100K annually in Crack Seal
Funding Model - 3% annually to Maintain Scope
Address Roads relative to PCI as benchmark
PCI Index updated every 5 years
Update the overall plan yearly
Complete Short/Gravel Roads with Remaining Funds
Industrial Roads (1 per year) beginning in 2017

## Slide 4
PROGRAM PRINCIPAL GUIDELINES
ROAD STABILIZATION COMMITTEE
  Pavement Condition Index (PCI)
  PCI derived from established measurements of pavement surface condition distresses and deficiencies
  0 to 100 scale, 100 being excellent
  PCI is one of the principal factors in treatment and scheduling
  Town wide assessment underway in 2022
  Report to BOS in early 2023

## Slide 5
PAVEMENT CONDITION INDEX
ROAD STABILIZATION COMMITTEE
TREATMENT BAND | PCI | Description
DO NOTHING | 93-100 | Excellent condition - in need of no maintenance.
ROUTINE MAINTENANCE | 86-92 | Good condition – may be in need of minor crack sealing or minor localized repair.
PREVENTIVE MAINTENANCE | 73-85 | Fair condition – pavement surface may be in need of surface sealing, full depth patch and/or crack sealing. Mill/overlay some areas
MILL and OVERLAY | 61-72 | Deficient condition – pavement surface structure in need of added strength for existing traffic. Typical repairs are overlay with or without milling.
RECONSTRUCTION | 0-60 | Poor condition – in need of base improvement. Typical repairs are reclamation or full depth reconstruction.
Chart: 
0-60 | 18.5
61-72 | 37.3
73-85 | 41.7
86-92 | 46.2
93-100 | 37.1

## Slide 6
Chart: 
0-60 | 18.5
61-72 | 37.3
73-85 | 41.7
86-92 | 46.2
93-100 | 37.1
PCI BREAKDOWN BY MILES
ROAD STABILIZATION COMMITTEE
93 - 100
86 - 92
73 - 85
61 - 72
00 - 60
10%

## Slide 7
TOTAL RECONSTRUCTION
Total Length = 13,496 LF
Total Cost = $3,521,625
TOTAL MILL / OVERLAY
Total Length = 19,039 LF
Total Cost = $978,375
Price per linear foot = $51.39
Price per linear foot = $260.94
$1----------$50----------$100----------$150----------$200----------$250--------$300
TREATMENT COST COMPARISON

## Slide 8
Chart: 
| 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
 | 1400000 | 520000 | 2575000 | 2145000 | 923000 | 2910000 | 5939314 | 5157000 | 5336899 | 4615000 | 4933450 | 4896054 | 4765332 | 4884103 | 4809103 | 4730677 | 4367277
$460,690
$443,604
$544,560
$327,674
$258,338
$442,628
$565,824
HISTORICAL FUNDING
~$170,484

## Slide 9
Chart: 
| 5 | 4 | 3 | 2 | 1 | 0
 | 0 | 2 | 2 | 4 | 2 | 10
65%
80%
ASPHALT
EXCAVATION
PIPE (HDPE)
7%
INFLATION

## Slide 10
ROAD STABILIZATION COMMITTEE
NORTHWESTERN DRIVE
2017 PCI = 62

## Slide 11
ROAD STABILIZATION COMMITTEE
WILSON STREET
2017 PCI = 50

## Slide 12
2023 ROAD LIST
ROAD STABILIZATION COMMITTEE

## Slide 13
RECOMMENDATION
“The Board of Selectmen adopts the 2023-2032 Road Program as proposed by the Road Stabilization Committee.”